## Slide 1: MIKE 11
Simulation Editor

## Slide 2: SIMULATION EDITOR
MIKE 11 Graphical User Interface (GUI)
The MIKE 11 graphical user interface is based on five ‘Editor’ interfaces
The main control editor is the ‘Simulation Editor’.
The simulation editor is the main control hub of a MIKE 11 simulation
Always leave the simulation editor open

## Slide 3: SIMULATION EDITOR
Simulation Editor (.sim11)
Cross Section Editor (.xns11)
Parameter Editor (.HD11)
Network Editor (.nwk11)
Time Series Editor (.dfs0)
Boundary Editor (.bnd11)
Access All Files Through the Simulation File
The Editors are synchronised together using the ‘Simulation Editor’
Synchronising the editors together enables links to be developed from one editor to another

## Slide 4: SIMULATION EDITOR
The simulation file contains all project information and provides dynamic links to all editors.
Always Create the Simulation File First
*.SIM11 File Extension
How? MIKE Zero -> File -> New -> File -> MIKE 11 -> Simulation (.sim11)

## Slide 5: SIMULATION EDITOR
The Model Tab specifies the type of model to be used and the simulation mode
Models Tab

## Slide 6: SIMULATION EDITOR
The Input Tab allows file specification based on model selections in the Model Tab
Browse for Files
Open Other Editors
Input Tab

## Slide 7: SIMULATION EDITOR
The Simulation Tab contains initial conditions, computational time step and simulation details
Select Type of Initial Conditions
(Steady State, Parameter File or Hotstart)
Calculates the Maximum Simulation
Period Based on Given Inputs
Select Time Step Type and Units
(Fixed, Tabulated or Adaptative)
Simulation Tab

## Slide 8: SIMULATION EDITOR
Adaptative Time Step
Tabulated Time Step
Uses Time Series (DFS0) File
Time Step Settings

## Slide 9: SIMULATION EDITOR
The Results Tab contains information on Results File names and saving frequency
Specify Name or Browse for File
Store Results as a Multiple of Time
Step or a Specific Time Interval (Seconds, Minutes, Hours or Days)
Results Tab

## Slide 10: SIMULATION EDITOR
Start Tab
Green Lights Indicate
All Inputs are Valid
A simulation cannot be started until all lights are green
The Start Tab contains information on validity of input data
Choice of running MIKE 11 with 2 different engines:
MIKE 11 “Classic”
MIKE 1D (new engine)
“Validation Messages” Display Error
Messages Indicated by the Red Status Light

## Slide 11: SIMULATION EDITOR
The Simulation File can be Edited in any Text Editor
Editable Text File