## Slide 1: MIKE 11
Results Viewing

## Slide 2: RESULTS VIEWING
MIKE 11
SIMULATION
Setting up and
running simulation
in MIKE Zero
Result files
Viewing and MIKE VIEW
extracting results Result Viewer
MIKE 11 (.res11)
MIKE 1D (.res1d)
Results Files and MIKE VIEW

## Slide 3: MIKE VIEW
MIKE 11 Results Files (.res11 and .res1d)
How? Start -> MIKE by DHI 20xx -> MIKE View -> MIKE View

## Slide 4: MIKE VIEW
Select Gridpoint
Mouse Location Selection
(Water Level or Discharge)
Add Multiple Series Using Right Click or Icons
Plot time series at gridpoints
How? MIKE View -> Plot -> TS in Gridpoints

## Slide 5: MIKE VIEW
Select Gridpoint
Summary Data for
All Gridpoints (Max/Min)
Tabular Data (Copy to External Software)
Plot time series at gridpoints
How? MIKE View -> Plot -> TS in Gridpoints

## Slide 6: MIKE VIEW
Change the Appearance of Plotted Data
Time Series View Options (TS Settings)
How? Time Series -> Right Click (Options)

## Slide 7: MIKE VIEW
MIKE 11 Bank Markers
(1, 2 & 3) Define Invert
and Bank Profiles (L & R)
Max Level (Dotted Red)
Use Mouse to Pick Branches
Animate Water Surface
Use SHIFT-Click and CTRL-Click to Control Profile Selection
Plot longitudinal profile of the river
How? MIKE View -> Plot -> Longitudinal Profile
Notes: Ctrl: stops the profile
Shift: unselects a branch

## Slide 8: MIKE VIEW
Longitudinal Profile Options (Axis)
How? Longitudinal Profile -> Right Click (Options)
Navigate through the different tabs

## Slide 9: MIKE VIEW
Longitudinal Profile Options (Graphical Items)
How? Longitudinal Profile -> Right Click (Options)
Add and animate multiple items and change display properties
Click here to add more items to be plotted on the profile

## Slide 10: MIKE VIEW
Longitudinal Profile Options (User Defined Indicators)
How? Longitudinal Profile -> Right Click (Options)
User defined indicators can be used to display calibration marks for example or to add annotations to the plot and highlight data.

## Slide 11: MIKE VIEW
Create and Save
Customised Plots
Customise Longitudinal Profiles

## Slide 12: MIKE VIEW
Draw Corresponding Time Series
Q-H Curve
How? MIKE View -> Plot -> Q-H Curve

## Slide 13: MIKE VIEW
Select Location with Mouse
Animate Water Level
MIKE 11 Bank Markers
Displayed
Minimum/Maximum
Levels Displayed
Cross Sections
How? MIKE View -> Plot -> Cross sections

## Slide 14: MIKE VIEW
Change Simple Display Settings Only
Cross Section View Options
How? Cross Section -> Right Click (Options)

## Slide 15: MIKE VIEW
All Animations
are Synchronised
Synchronise Plots and Animations