## Slide 1: 1D HYDRODYNAMIC THEORY
MIKE 11

## Slide 2: Hydrodynamics
Fundamentals
PHYSICAL SYSTEM
River Network
Floodplains
Structures
PHYSICAL LAWS
Conservation of Mass
Conservation of
Momentum
SCHEMATISE
Represent by a simple
Equivalent System
DISCRETISE
Express as a Finite
Difference Relation
NUMERICAL MODEL
Modelling of unsteady flow is based on three fundamental elements:
A differential relationship
expressing the physical
laws
A finite difference scheme
producing a system of
algebraic equations
A mathematical algorithm
to solve these equations

## Slide 3: Hydrodynamics
Saint Venant Equations
General Assumptions:
Incompressible and homogeneous fluid
Flow is one-dimensional (uniform velocity and water level in cross-section)
Bottom slope is small
Small longitudinal variation in geometry
Hydrostatic pressure distribution
Conservation of Mass
Conservation of Momentum
Conservation of Mass
(Continuity Equation)
Conservation of Momentum (Momentum Equation)

## Slide 4: Hydrodynamics
Net increase of Mass from Time1 to Time2 =
Net Mass Flux into control volume (Time1 to Time2) +
Net Mass Flux out of control volume (Time1 to Time2)
dx
Q
at time t
at time t+dt
h (t)
h (t+dt)
Conservation of Mass (Continuity Equation)

## Slide 5: Hydrodynamics
Conservation of Momentum (Momentum Equation)
Net increase of Momentum from Time1 to Time2 =
Net Momentum Flux into control volume (Time1 to Time2) +
Sum of external forces acting over the same time
G
dx
h (t)
F
P
P + dP
z (t)
H

## Slide 6: Hydrodynamics
Momentum = Mass per unit length * Velocity
Momentum Flux = Momentum * Velocity
Pressure Force = Hydrostatic Pressure P
Friction Force = Force due to Bed Resistance
Gravity Force = Contribution in X-direction
Momentum = Momentum Flux + Pressure - Friction + Gravity
Elements of the Momentum Equation

## Slide 7: Hydrodynamics
Momentum:
Momentum Flux:
Pressure Term:
Friction Term:
Gravity Term:
Elements of the Momentum Equation

## Slide 8: Hydrodynamics
Kinematic Wave
Diffusive Wave
Fully Dynamic Wave
Solving the Differential Momentum Equation

## Slide 9: Wave approximations
Kinematic and Diffusive Wave
Diffusive Wave:
Includes:
1. Bed Friction Term
2. Gravity Term
3. Hydrostatic Gradient Term
Applications:
+ Relatively Steady Backwater Effects
+ Slowly Propagating Flood Waves
- Tidal Flows NOT applicable
Kinematic Wave:
Includes:
1. Bed Friction Term
2. Gravity Term
Applications:
+ Steep Rivers
- Backwater Effects NOT applicable
- Tidal Flows NOT applicable

## Slide 10: Wave approximations
Fully Dynamic Wave:
Includes:
1. Bed Friction Term
2. Gravity Term
3. Hydrostatic Gradient Term
4. Acceleration Term
Applications:
+ Fast Transients
+ Tidal Flows
+ Rapidly changing backwater effects
+ Flood waves
Fully Dynamic Wave
HIGHER ORDER
FULLY DYNAMIC WAVE:
Modified Bed Friction Term
Steep Channels

## Slide 11: Finite difference scheme
6 Point Abbott-Ionescu FD Scheme
Q
Q
Q
h
h
h
h
MIKE11/MOUSE is fully implicit; the finite difference scheme features:
h-points at every cross- section and junction
q-points between h-points and at structures
Solve the continuity equation between q-points
Solve the momentum equation between h-points
Continuity Equation
Momentum Equation
At structures, momentum equation replaced by the energy equation

## Slide 12: Finite difference scheme
Continuity Equation centered around h-points
Momentum Equation centered around Q-points
6 Point Structure

## Slide 13: Model stability
Given: Initial Conditions and Finite Difference Approximation which is consistent
Then: Stability is the necessary and sufficient condition for convergence
Conditional stability is achieved for Courant Number < 1
Example: D=10, V=1, dX=1000
Courant Number:
Courant Condition
Notes: In order to keep the solution of the finite difference solution numerically stable different criteria must be observed