## Slide 1: MIKE 11
Model Stability, Tips & Tricks

## Slide 2: STABILITY, TIPS & TRICKS
Model Stability, Tips and Tricks

## Slide 3: STABILITY, TIPS & TRICKS
Stability Criteria (Courant Number)
The Courant Number (Cr) describes the Relationship between:
the Speed of Physical Disturbances in the System, and
the Speed at which Disturbances Travel in the Numerical Model
Courant Number:
Physical Propagation Speed
Max Numerical Propagation Speed

## Slide 4: STABILITY, TIPS & TRICKS
Spatial and Temporal Constraints
Space Step (Δx)
Δx needs to be small enough to resolve changes in channel width and rapid changes in the water surface profile
Small Δx can result in high Courant numbers
Small Δx normally corresponds to a small Δt
Time Step (Δt)
Requirement for a small Δt can be symptomatic of poor model schematisation
Selection of Δt should be based on time varying characteristics of the system (ie. tidal models, Δt < 15 mins)
Very rapidly changing flow (ie dambreak) will require a small Δt
The Courant Criteria can be used to set an Upper Bound on the Time Step (Δt) based on a given Spatial Resolution (Δx)

## Slide 5: STABILITY, TIPS & TRICKS
Enhancing Stability
To increase the stability of the system
Decrease the Time Step (Δt)
Increase the Space Step (Δx) (particularly near structures)
Use different Wave Approximation (ie. Kinematic Wave for Steep Reaches)
Use Weirs/Links Channels at Confluences with Different Invert Levels
Increase Number of Iterations per Time Step
Increase Number of Iterations at Structures
Change Default Values (Delta & Zeta Min)
Recalculate levels of processed data of cross-sections
Increases Simulation Time
Decreases Simulation Time

## Slide 6: STABILITY, TIPS & TRICKS
Default Values (Delta)
d = 0.5, FD Scheme is Fully Centred
Equal Emphasis on t n and t n+1
d > 0.5, Stabilising Effect but also Dissipative
d = 1.0, FD Scheme is Forward Centred
All Emphasis on t n+1
Model Type | Delta Range
Tidal | 0.50 – 0.60
Upland River | 0.50 – 0.70
Large River | 0.50 – 0.80
Steady State | 0.50 – 1.00

## Slide 7: STABILITY, TIPS & TRICKS
Default Values (Zeta Min)
ξmin Minimum value of the sum of calculated head loss factors (at structures)
ΔH = ξ(V2/2g),
where: ξ = Σ(ξin, ξout, bend…)
Increasing ξmin
Stabilises structure solution, but also has the effect of introducing higher head losses at structures
Structures with a Very Small
Head Loss Can Cause Instability
in the Model – Consider Removing

## Slide 8: STABILITY, TIPS & TRICKS
Tips for Structures
Closed cross sections
Broad Crested Weirs:
Insert Wedge in Base so that Flow can Commence Gradually
Long Culverts:
Use Closed Sections instead of Structure to account for Friction effects
Use Small Dx to develop water surface profile inside long culvert
Tabular Data:
If changes are made to Sections U/S or D/S of a Structure, remember to Recalculate Q/h relations
Make sure Q/h relations are Monotonically increasing
Add more levels to the Q/h relations when necessary

## Slide 9: STABILITY, TIPS & TRICKS
Tips at Confluences
Important to Define Cross-Section Changes at Confluences:
MIKE11 will copy (extrapolate) nearest Cross-Section to Branch End if no Cross-Section Exists
In Longitudinal Profiles (MIKE View) Branch Ends with no Cross-Section will be assigned Invert Level of Zero
MIKE11 will interpolate Cross-Section at Junctions if no Cross-Section Exists
Preferable to Copy/Move to prevent Unrealistic Extrapolations or Interpolations
Take Care When Graphically Connecting Branches:
A Junction forces a H-point in the Scheme
Graphical Connection Tool snaps to Cross-Sections and Digitised Points (very small Δx can occur)

## Slide 10: ADDITIONAL FEATURES
res11read programme
Small utility to read and export MIKE 11 res11 files to text format.
Found under C:\Program Files (x86)\DHI\20xx\bin\ res11read.exe
More info:
- Appendix B, MIKE 11 User Manual
Tips and Tricks page on DHI website
  Res11read.exe’ 64-bit since release 2012: Extraction possible from large result-files (> 1GB)

## Slide 11: GETTING HELP IN MIKE 11
Help Menu: Access the Help from any editors by pressing the F1 Key
Manuals:
  MIKE 11 User Manual
  MIKE 11 Reference Manual
  MIKE Zero Manuals
For an easy access to all manuals available, open the Documentation Index
How? Start > Programs > MIKE by DHI 20xx > MIKE Zero > Documentation > MIKE 11 Documentation Index

## Slide 12: MIKE 11 DOCUMENTATION INDEX

## Slide 13: MORE WAYS TO FIND HELP
Install and check the examples that come with each programme
FAQ Page on DHI’s website http://faq.dhigroup.com
Tips and Tricks Page on DHI’s website http://tips.dhigroup.com