## Slide 1: MIKE 11
Control Structures

## Slide 2: CONTROL STRUCTURES
Complex Operations and Regulation

## Slide 3: CONTROL STRUCTURES
Control structure used whenever the flow through a structure is to be regulated by the operation of a movable gate (sluice gate, underflow gate, radial gate) or the flow is controlled directly as in the case of pump or turbine
Setting up a control structure in MIKE 11 is defining a CONTROL STRATEGY
The control strategy is the sequence of commands or rules that determine the way a structure can be operated in MIKE 11
A structure can have any number of strategies defined by a sequence of conditions that must be evaluated as TRUE or FALSE

## Slide 4: CONTROL STRUCTURES
Defined in the Network File
How? Network File -> View -> Tabular View -> Structures Page
Control Structure Types:
Underflow Gate (Sluice Gates)
Overflow Gates (Inflatable Dams and Movable Weirs)
Radial Gates (Dam Spillways)
Discharge Control (Pumps, Turbines)

## Slide 5: CONTROL STRUCTURES
Underflow Gates (Sluice)

## Slide 6: CONTROL STRUCTURES
Radial Gates (Spillways)

## Slide 7: CONTROL STRUCTURES
Implemented with a Control Strategy
Logical statements that define the conditions for implementing the strategy
The settings (or Target Point ) for the structure as a function of the Control Point
A Control Strategy consists of:
A Control Definition
A Control Rule
Logical statements that define the conditions for implementing the strategy
The settings (or Target Point ) for the structure as a function of the Control Point

## Slide 8: CONTROL STRUCTURES
Logical Decision Tree – Control Strategy
Priority 1 Logicals
Priority 2 Logicals
Priority N Logicals
Always True
True
True
False
False
Strategy 1
Strategy 2
Strategy N
Start (for each time step)
Set Gate

## Slide 9: CONTROL STRUCTURES
Control and Target Points
A Control Point is the Variable used to Determine the Target Function:
Flood levels
Reservoir Inflows
Time of year
A Target Point is the Variable
Being Set:
Gate level
Reservoir level
Discharge
Variable Types:
Water level (H)
Water level difference (dH)
Discharge (Q)
Discharge difference (dQ)
Sum of discharges
Velocities (V)
Volumes
Concentrations
Calendar
Time-series

## Slide 10: CONTROL STRUCTURES
Calculation Modes
Calculation Modes for Control Structures:
Direct Gate Operation (Tabulated, Closed, Open, Set Equal to, etc)
PID Control (Proportional Integral Derivative)
Momentum Equation
Iterative Solution
Water Level
Gate Level

## Slide 11: CONTROL STRUCTURES
Control Structure Page in Network File
Attributes Tab
Overview of all Control Structures in the Model
Control Definitions Tab

## Slide 12: CONTROL STRUCTURES
Attributes Tab (Overflow, Underflow and Discharge)
Standard Head Losses Apply to All

## Slide 13: CONTROL STRUCTURES
Attributes Tab (Radial Gate and Sluice/Formula)

## Slide 14: CONTROL STRUCTURES
Control Definitions Tab
Calculation Modes

## Slide 15: CONTROL STRUCTURES
Time dependent control strategies
New option in release 2012
Tabulated control strategies as function of time
Example: Rating curve value depending on day of year

## Slide 16: CONTROL STRUCTURES
Control Structures Notes
Allows for defining highly advanced and complex control and regulation strategies (Reservoir outlet optimization, Irrigation, Flood control etc.)
For stability - as for all other structures: Ensure that structure geometry (width and sill level) are always smaller than up- and downstream sections
Geometry limitation: Structures of constant width