## Slide 1: MIKE 11
Floodplain Modelling and Quasi 2D

## Slide 2: FLOODPLAIN MODELLING
Floodplain Modelling Options:
1D:
  Lump River and Floodplain as Single branch
  Simple 1D River Model in MIKE 11
  Branched and Looped Network in MIKE 11
  Floodplain as part of the cross-section in MIKE 11
  Floodplain computed as additional storage in cross-sections in MIKE 11
  Limitation: Same Water Levels in River and Floodplain
Quasi 2D:
  River and Floodplain separate Flow Paths
  Requires accurate and detailed Data
  Relevant for:
    Flood Mapping
    Floodplain Inundation and Drainage Modelling
    Flood Damage assessments

## Slide 3: FLOODPLAIN MODELLING
Looped and Quasi-2D Networks

## Slide 4: FLOODPLAIN MODELLING
Simple 1D River Model
RIVER CROSS-SECTIONS
SIMPLE 1-D RIVER MODEL
RIVER CROSS-SECTIONS
RIVER CROSS-SECTIONS

## Slide 5: FLOODPLAIN MODELLING
Branched and Looped Network
LOOPED RIVER NETWORK
TRIBUTARIES
GREATER SCHEMATISATION (1D)

## Slide 6: FLOODPLAIN MODELLING
Floodplain Model (Quasi 2D)
PARALLEL RIVERS
FLOODED AREAS
LINK CHANNELS
FLOODPLAIN MODEL (QUASI 2-D)

## Slide 7: FLOODPLAIN MODELLING
Schematisation (One-Dimension)

## Slide 8: FLOODPLAIN MODELLING
Schematisation of Floodplains (Quasi 2D)

## Slide 9: FLOODPLAIN MODELLING
Inundation Flow Network

## Slide 10: FLOODPLAIN MODELLING
Integrated Flood Plain

## Slide 11: FLOODPLAIN MODELLING
START:
Do the spill areas convey
significant flow discharges ?
Does the river spill?
Flood plain model not needed
Are levees present ?
Are spill flows conveyed
parallel to the river ?
Flood Cell with
link channel
Are levees present ?
Additional
Flooded
Area
Flood plain
attached to
cross section
Is the flood plain flow frequently
interrupted by roads and other
flow obstructions?
Interlinked Flood Cells
Routing Channels
1D
Q 2D
N
Y
N
N
N
N
Y
Y
Y
Y
Y
N

## Slide 12: FLOODPLAIN MODELLING
Differences Between 1D and Quasi 2D
1D:
Channel and Floodplain lumped together in Single Cross-Section
One Water Level and Velocity Applies to both Channel and Floodplain
Quasi 2D:
River and Floodplain Separate Flow Paths
Requires Accurate and Detailed Data
Relevant for:
Floodplain Inundation and Drainage Modelling
Flood Mapping and Damage Assessments

## Slide 13: FLOODPLAIN MODELLING
Floodplain Schematisation Options
River
Floodplain
River
Floodplain
River
Floodplain
River
Floodplain ?
FP2: Added Storage
FP3: Part of the Cross-Section
FP4: Separated from the River
FP1: Ignored
Link channel

## Slide 14: FLOODPLAIN MODELLING
Floodplain Schematisation Options
FP1 :
FP2 :
FP3 :
FP4 :
•
?
?
•

## Slide 15: FLOODPLAIN MODELLING
FP2: Added Storage
Used to Account for Areas in the Floodplain that will affect Water Levels in the Main Channel
Applied Through Processed Data Tables as Area At Different Levels

## Slide 16: FLOODPLAIN MODELLING
FP3: Part of the Cross-Section
Floodplain Geometry can be Assigned Different Resistance Values to Reduce Conveyance
Applied Through Raw Data Tables as Roughness or Factor

## Slide 17: FLOODPLAIN MODELLING
FP4: Separated from the River
River Channel and Floodplains Modelled Separately
Link Channels Define Flow Exchange between Branches
Link Channels have no Storage and behave like Weirs
U/S Bed Level
D/S Bed Level
U/S Chainage
D/S Chainage
Link Structure
Connection to
River Branch
Connection to
Floodplain Cell
or Branch
River
Floodplain
Manning's Coefficient

## Slide 18: FLOODPLAIN MODELLING
Floodplain Inundation
No Flooding: FL1 : Local Rainfall Flooding FL2 : Flooding via local depressions FL3 : Flooding via Levees
River
High ground
No Flooding
FL3
FL2
FL1

## Slide 19: FLOODPLAIN MODELLING
Floodplain Inundation
Flood Plain
River
Levee
Flood Plain
River
Channels
DR1
DR2
DR1 : Drainage via Channel DR2 : Drainage via Levees

## Slide 20: FLOODPLAIN MODELLING
Duplicate Storage at Junctions
In Complex Networks there is Potential for Duplicate Storage at Junctions
Schematisation might need to be Adjusted
Use Link Channels which have no Storage

## Slide 21: FLOODPLAIN MODELLING
Model Storage:
Calculated from Cross Section Width:
User Defined Storage:
Total Surface Storage = Storage width*dx + Add. Storage
dx
1
dx
2
dx
1
/2
dx
2
/2
b
1
b
2
b
3
A
s
=b
2
(dx
1
/2+dx
2
/2)

## Slide 22: FLOODPLAIN MODELLING
Schematisation of Junctions
Ensure that the Lowest Point of each Cross-Section is a Similar Level
If Bed Levels are Significantly Different, use Link Channels to Connect
River 1
River 2
River 3