## Slide 1: MIKE 11
Coupling RR with HD through the River Network
Rainfall Runoff (RR) Modelling

## Slide 2: Coupling RR-HD

## Slide 3: Coupling RR-HD
MODELS AVAILABLE:
NAM – daily or hourly, with surface & subsurface interflow & storages, nine cal. Parameters
SMAP – monthly, with two storages, five cal. parameters (similar accuracy to monthly NAM)
UHM – unit hydrograph method using SCS or user defined curves and SCS or standard loss models
Urban – two methods: time/area or non-linear reservoir
FEH – UK Flood Estimation Handbook, with design or observed flood events
DRiFt – DEM-based morphological model developed by CIMA (Italian research cooperative)

## Slide 4: Coupling RR-HD
Basic principles :
Using the rainfall runoff module as boundary condition for the hydrodynamics
Coupling at branch ends
Coupling along reaches
Ensuring that the hydrodynamic setup is well defined

## Slide 5: Coupling RR-HD
The physical system
4 catchments
1 main stream
3 tributaries
1 higher order branch
How do we represent this in the model?
C2
C1
C3
C4

## Slide 6: Coupling RR-HD
The Rainfall Runoff system
C2
C1
C3
C4
Model each sub- catchment separately
May use same set of parameters for all 4
Subdivision to ensure timing in HD correct

## Slide 7: Coupling RR-HD
The Hydrodynamic system
Set up the hydrodynamics
Stand alone
Background flow
Boundary conditions for all free branch ends
Please ensure that the hydrodynamic system is sound
Must be able to run without Rainfall Runoff input

## Slide 8: Coupling RR-HD
Coupling the two systems
C2
C1
C3
C4
Runoff may be coupled
as a point source
as a distributed source
How do we couple the same catchment to multiple branches?

## Slide 9: Coupling RR-HD
One catchment to multiple branches
A1C3+ A2C3=AC3
Runoff may be distributed over multiple branches by catchment area weighting
C3
A1C3
A2C3

## Slide 10: Coupling RR-HD
IMPLEMENTATION :
Solution A : RR coupled to HD model (simultaneous simulations)
          Tick both HD and RR
          Specify a RR11 model file
MULTIPLE OF HD TIME STEP

## Slide 11: Coupling RR-HD
IMPLEMENTATION :
Solution B : Independent simulations
          Specify previous RR results on Input page

## Slide 12: Coupling RR-HD
Links defined in the Network file :
Two ways of coupling :
Point source
Distributed source
For multiple branches in a catchment, distribute by catchment area weighting